## Slide 1: Ideas XML for IDS (v 00.1)
Arie van Kranenburg

## Slide 2: Apologies for the somewhat raw presentation
I started with the design last saterday (first day after Friday meeting)
I had to do some other work too
I changed the XML design during the preparation of the presentation
So:
The examples are not complete (but clear enough, I hope)
There will be spelling failures
There will be some syntax errors (Powerpoint has no syntax checking)
Refinements are needed

## Slide 3: Keep in mind
The XML is the schema for the IFC propertysets
An XSD is just for validating the XML
We need other tools for validating the IFC
We need “plugin” for the different authoring systems
We need tools for defining IDS XML definitions
But in the first step a XML-editor will do the job

## Slide 4: IFC property inheritance (0.01: Only SingleValue)
IfcProperty (A)
IfcComplexProperty
IfcSimpleProperty (A)
IfcPropertyBoundedValue
IfcPropertyEnumerated
IfcPropertyListValue
IfcPropertyReferenceValue
IfcPropertySingleValue
IfcPropertyTableValue

## Slide 5: Enumeration also mapped on SingleValue
Enumeration only known outside the IFC file
This needs a mapping for the standard properties (later)

## Slide 6: Types in version 0.1 (based on IFC2x3)
type IFC type definition
integer IfcInteger Defined type of simple type INTEGER.
real IfcReal Defined type of simple type REAL.
boolean IfcBoolean Defined type of simple type BOOLEAN.
? IfcLogical Defined type of simple type LOGICAL.
id IfcIdentifier Defined type of simple type STRING for identification purposes.
label IfcLabel Defined type of simple type STRING for naming purposes.
text IfcText Defined type of simple type STRING for descriptive purposes.

## Slide 7: Why 3 types of string?
IFC uses them for different purposes
IfcIdentifier for identification
IfcLabel for naming
IfcText for descriptions (but not always)
In IFC4 the length is maximized
  IfcIdentifier STRING[255]
  IfcLabel STRING[255]
  IfcText STRING[32767]
The definitions of IfcIdentifier and IfcLabel are identical

## Slide 8: Starting point
Agreements of last friday
Short tag names, can be changed
Attributes for ID’s, references, types, values and units
Elements for names and descriptions
Can we do the attribute/element discussion later?

## Slide 9: What’s not in (for now)
Multi-language support
Hierarchical classification
Mapping properties on standard psets
Rule checking

## Slide 10: Information included in v 0.01
Units
Items for enumerations (predefined name values)
Properties
  type: integer/real/boolean/id/label/text
  unit: reference to a specific unit
PropertySets (set of properties)
Classes
  IFC mapping on the subtype of IfcElementType
  Pset of the ElementType
  Pset of the Element (instance)
All elements can have ID and name

## Slide 11: Proposal overall structure of the XML definition
<?xml version="1.0" encoding="utf-8"?>
<IDS>
<header>
<version>0.1</version>
<!--PM to be completed later-->
</header>
<units>
<unit>...</unit>
<!--more units-->
<unit>...</unit>
</units>
<enums>
<enum>...</enum>
<!--more enums-->
<enum>...</enum>
</enums>
<properties>
<prop>...</prop>
<!--more properties-->
<prop>...</prop>
</properties>
<psets>
<pset>...</pset>
<!--more propertysets-->
<pset>...</pset>
</psets>
<classes>
<class>...</class>
<!--more classes-->
<class>...</class>
</classes>
</IDS>

## Slide 12: Units
<units>
<unit ID=‘mmID'>
<name>millimetre</name>
<abbr>mm</abbr>
</unit>
<unit ID='litreID'>
<name>litre</name>
<abbr>l</abbr>
</unit>
<unit ID='WattID'>
<name>Watt</name>
<abbr>W</abbr>
</unit>
</units>

## Slide 13: Enums (example is Status property in IFC)
<enums>
<enum ID='NewID'>
<name>New</name>
</enum>
<enum ID='ExistingID'>
<name>Existing</name>
</enum>
<enum ID='DemolishID'>
<name>Demolish</name>
</enum>
<enum ID='TemporaryID'>
<name>Temporary</name>
</enum>
</enums>

## Slide 14: Properties (of element types)
<prop ID='HeatEmissionID' type='real' unit='WattId'>
<name>Heat emission EN442 75/65/20</name>
<desc>Heat emission with an input temperature of 75 degrees, etc<desc>
</prop>
<prop ID='WaterContentID' type='real' unit='LitreID'>
<name>Water content</name>
</prop>
<prop ID='PanelTypeID' type='integer'>
<name>Panel type</name>
<enum val='10'/>
<enum val='11'/>
...
<enum val='44'/>
</prop>

## Slide 15: Properties (of elements)
<prop ID='RequiredOutputID' type='real' unit='WattId'>
<name>Required output</name>
<desc>Required heat emission of this particular radiator<desc>
</prop>
<prop ID='StatusID' type='label'>
<name>Status</name>
<enum ref='NewID'/>
<enum ref='ExistingID'/>
<enum ref='DemolishID'/>
<enum ref='TemporaryID'/>
</prop>

## Slide 16: Propertysets (just a set of properties)
<pset ID='PanelRadiatorTypePsetID'>
<name>Panel radiator type properties</name>
<prop ref='HeatEmissionID'/>
<prop ref='WaterContentID'/>
<prop ref=‘PanelTypeID'/>
</pset>
<pset ID='PanelRadiatorPsetID'>
<name>Panel radiator properties</name>
<prop ref='RequiredOutputID'/>
<prop ref='StatusID'/>
</pset>

## Slide 17: Class (generic part)
<class ID='PanelRadiatorID'>
<name>Panelradiator</name>
<desc>Body made of steel filled with water to heat a space<desc>
type and element part (see next sheet)
</class>

## Slide 18: Class (type/element part with IFC mapping)
<etyp>
<pset ref='PanelRadiatorTypePsetID'/>
<map2>
<ifc2>IFCSPACEHEATERTYPE/PANELRADIATOR</ifc2>
<ifc4>IFCSPACEHEATERTYPE/RADIATOR</ifc4>
<ifc5>IFCELEMENTTYPE/PanelRadiator</ifc5>
</map2></etyp>
<elem>
<pset ref='PanelRadiatorPsetID'/>
<map2>
<ifc2>IFCENERGYCONVERSIONDEVICE</ifc2>
<ifc4>IFCSPACEHEATER</ifc4>
<ifc5>IFCELEMENT</ifc5>
</map2></elem>

## Slide 19: Relation between element and type is fixed!
ElementType
IFC2 IFCSPACEHEATERTYPE
IFC4 IFCSPACEHEATERTYPE
IFC5 IFCELEMENTTYPE
Element
IFCENERGYCONVERSIONDEVICE
IFCSPACEHEATER
IFCELEMENT

## Slide 20: Class (Panel radiator)
<class ID='PanelRadiatorID'>
<name>Panel radiator</name>
<desc>Body made of steel filled with water to heat a space<desc>
<etyp>
<pset ref='PanelRadiatorTypePsetID’/>
</etyp>
<elem>
<pset ref='PanelRadiatorPsetID’/>
</elem>
<ifc2>IFCSPACEHEATERTYPE/PANELRADIATOR</ifc2>
<ifc4>IFCSPACEHEATERTYPE/RADIATOR</ifc4>
<ifc5>IFCELEMENTTYPE/PanelRadiator</ifc5>
</class>

## Slide 21: Possibilities for ID
Descriptive name
UID (local unique)
GUID (global unique)
URI (web-adress-like)
All are possible with the same XML definition, it’s just content

## Slide 22: Using descriptive name as ID
This is already the case for the standard Psets
No plug-in needed at the receiving side (viewer)
Let we see what happens to the XML then

## Slide 23: Name=ID 1: units and props (no enums needed)
<units>
<unit ID='mm’/> <unit ID='l’/> <unit ID='W’/>
</units>
<props>
<prop ID='Heat emission EN442 75/65/20' type='real' unit='W’/>
<prop ID='Water content' type='real' unit=‘l’/>
<prop ID='Panel type' type='integer’>
  <enum val='10’/>...<enum val='44'/></prop>
<prop ID='Required output' type='real' unit='W’/>
<prop ID='Status' type='label’>
<enum val='New’/> <enum val='Existing'/>
<enum val='Demolish’/> <enum val='Temporary'/></prop>
</props>

## Slide 24: Name=ID 2: psets and classes
<psets>
<pset ID='Panel radiator type properties'>
<prop ref='Heat emission EN442 75/65/20'/>
<prop ref='Water content'/>
<prop ref='Panel type'/></pset>
<pset ID='Panel radiator properties'>
<prop ref='Required output'/>
<prop ref='Status'/></pset></psets>
<classes>
<class ID='Panel radiator'>
<etyp><pset ref='Panel radiator type properties'/></etyp>
<elem><pset ref='Panel radiator properties'/></elem>
<ifc2>IFCSPACEHEATERTYPE/PANELRADIATOR</ifc2>
</class><classes>

## Slide 25: Propertysets in the IFC-file (schematic)
#1=IFCPROPERTYSINGLEVALUE('HeatEmissionID',$,IFCREAL(1785.0),$);
#2=IFCPROPERTYSINGLEVALUE('WaterContentID',$,IFCREAL(10.2),$);
#3=IFCPROPERTYSINGLEVALUE('PanelTypeID',$,IFCINTEGER('22'),$);
#5=IFCPROPERTYSET(... ,'PanelRadiatorTypePsetID',$,(#1,#2,#3));
#6=IFCSPACEHEATERTYPE(... ,(#5), ... ,.PANELRADIATOR.);
#10=IFCPROPERTYSINGLEVALUE('RequiredOutputID',$,IFCREAL(1250.0),$);
#20=IFCPROPERTYSINGLEVALUE('StatusID',$,IFCLABEL('NewID'),$);
#50=IFCPROPERTYSET(... ,'PanelRadiatorPsetID',$,(#10,#20));
#60=IFCENERGYCONVERSIONDEVICE (...);
#61=IFCRELDEFINESBYTYPE (...,(#60),#6);
#62=IFCRELDEFINESBYPROPERTIES (...,(#60),#50);

## Slide 26: Propertysets in the IFC-file (GUID, XML needed)
#1=IFCPROPERTYSINGLEVALUE('c6f94d46-31f2-4f76-ab6d-f76564291972',$,IFCREAL(1785.0),$);
#2=IFCPROPERTYSINGLEVALUE('f0d3fa44-f093-4058-9d70-d2e3f51b51ba',$,IFCREAL(10.2),$);
#3=IFCPROPERTYSINGLEVALUE('a7e1e6f8-4f9b-4294-9cfa-aac25cc2d3a0',$,IFCINTEGER('22'),$);
#5=IFCPROPERTYSET(... ,'cfdfb8b8-40e4-469a-9b0f-21aa6fb82a40',$,(#1,#2,#3));
#6=IFCSPACEHEATERTYPE(... ,(#5), ... ,.PANELRADIATOR.);
#10=IFCPROPERTYSINGLEVALUE('a7e1e6f8-4f9b-4294-9cfa-aac25cc2d3a0',$,IFCREAL(1250.0),$);
#20=IFCPROPERTYSINGLEVALUE('6ac1d4ef-a11b-43b7-b776-652cc988d826',$,IFCLABEL('8432189f-etc
#50=IFCPROPERTYSET(... ,'b3c8de80-4a62-4fe0-af4a-e70f3909a62f',$,(#10,#20));
#60=IFCENERGYCONVERSIONDEVICE (...);
#61=IFCRELDEFINESBYTYPE (...,(#60),#6);
#62=IFCRELDEFINESBYPROPERTIES (...,(#60),#50);

## Slide 27: Propertysets in the IFC-file (names as ID)
#1=IFCPROPERTYSINGLEVALUE('Heat emission EN442 75/65/20 [W]',$,IFCREAL(1785.0),$);
#2=IFCPROPERTYSINGLEVALUE('Water content [l]',$,IFCREAL(10.2),$);
#3=IFCPROPERTYSINGLEVALUE('Panel type',$,IFCINTEGER('22'),$);
#5=IFCPROPERTYSET(... ,'Panel radiator type properties',$,(#1,#2,#3));
#6=IFCSPACEHEATERTYPE(... ,(#5), ... ,.PANELRADIATOR.);
#10=IFCPROPERTYSINGLEVALUE('Required output [W]',$,IFCREAL(1250.0),$);
#20=IFCPROPERTYSINGLEVALUE('Status',$,IFCLABEL('New'),$);
#50=IFCPROPERTYSET(... ,'Panel radiator properties',$,(#10,#20));
#60=IFCENERGYCONVERSIONDEVICE (...);
#61=IFCRELDEFINESBYTYPE (...,(#60),#6);
#62=IFCRELDEFINESBYPROPERTIES (...,(#60),#50);

## Slide 28: Mapping on/of standard psets
Standard Pset’s have measures, no units
It is possible to define them with the IDS XML
They will stay compliant to the IFC standard
But mapping on the IFC measures have to be added (later)
It is possible to skip unwanted properties (subset)

## Slide 29: Pset_ManufacturingTypeInformation

## Slide 30: Pset_ManufacturingTypeInformation (in IDS XML)
<prop ID='ArticleNumber' type='id'>
<name>Article number</name>
<desc>Article number or reference that may be applied to a product...</desc></prop>
<prop ID='ModelReference' type='label'>
<name>Item name</name>
<desc>The name of the manufactured item as used by the manufacturer</desc></prop>
<prop ID='ModelLabel' type='label'>
<name>Model line</name>
<desc>The model number and/or unit designator assigned by the m…</desc></prop>
<prop ID='Manufacturer' type='label'>
<name>Manufacturer name</name>
<desc>The organization that manufactured and/or assembled the item</desc></prop>
<prop ID='ProductionYear' type='label'>
<name>Model year</name>
<desc>The year of production of the manufactured item</desc></prop>

## Slide 31: But now in Dutch (ID acc. IFC, name in Dutch)
<prop ID='ArticleNumber' type='id'>
<name>Artikelcode</name></prop>
<prop ID='ModelReference' type='label'>
<name>Productnaam</name></prop>
<prop ID='ModelLabel' type='label'>
<name>Serie</name></prop>
<prop ID='Manufacturer' type='label'>
<name>Fabrikant</name></prop>
<prop ID='ProductionYear' type='label'>
<name>Modeljaar</name></prop>

## Slide 32: Name of the Pset also in Dutch
<pset ID='Pset_ManufacturerTypeInformation'>
<name>Productinformatie</name>
<prop ref='ArticleNumber'/>
<prop ref='ModelReference'/>
<prop ref='ModelLabel'/>
<prop ref='Manufacturer'/>
<prop ref='ProductionYear'/>
</pset>

## Slide 33: Standard Pset added tot Class definition (etyp)
<class ID='PanelRadiatorID'>
<name>Panel radiator</name>
<desc>Body made of steel filled with water to heat a space<desc>
<etyp>
<pset ref='PanelRadiatorTypePsetID’/>
NEW <pset ref='Pset_ManufacturerTypeInformation’/>
</etyp>
<elem>
<pset ref='PanelRadiatorPsetID’/>
</elem>
<ifc2>IFCSPACEHEATERTYPE/PANELRADIATOR</ifc2>
<ifc4>IFCSPACEHEATERTYPE/RADIATOR</ifc4>
<ifc5>IFCELEMENTTYPE/PanelRadiator</ifc5>
</class>

## Slide 34: No property names in Dutch (as it is now)
#1=IFCPROPERTYSINGLEVALUE('ArticleNumber',$,IFCIDENTIFIER('440.355.00.2'),$);
#2=IFCPROPERTYSINGLEVALUE('ModelReference',$,IFCLABEL('Duofix element voor massiefbouw, 112 cm'),$);
#3=IFCPROPERTYSINGLEVALUE('ModelLabel',$,IFCLABEL('Duofix'),$);
#4=IFCPROPERTYSINGLEVALUE('Manufacturer',$,IFCLABEL('Geberit'),$);
#5=IFCPROPERTYSINGLEVALUE('ModelYear',$,IFCLABEL('2020'),$);
#6=IFCPROPERTYSET(... ,'Pset_ManufacturerTypInformation',$,(#1,#2,#3,#4,#5));
Dutch shows up in the values (the green ones), not in the property names

## Slide 35: But in a receiving application it can be
Productinformatie
Artikelcode 440.355.00.2
Productnaam Duofix element voor massiefbouw, 112 cm
Serie Duofix
Fabrikant Geberit
Modeljaar 2020
No blue items anymore
But the application have to use the XML definition

## Slide 36: Local addition of enums (FireRating)
<prop ID='FireRating' type='label’>
<name>Brandwerendheid WBDBO</name>
<enum val='geen'/>
<enum val='30 min'/>
<enum val='60 min'/>
<enum val='90 min’/>
</prop>
NB The type of FireRating is label, so no unit min.!
There are just 3 rating levels, there is no 45.3 min.
There is also not something like 0 min, just no rating
With this enumeration the following is not correct: 30m or 60 minuten

## Slide 37: Adding multi-language support (later)
<name lang='EN'>Panelradiator</name>
<name lang='NL'>Paneelradiator</name>
<name lang='DE'>Flachheizkörper</name>
<name lang='FI'>Paneeliradiaattori</name>

## Slide 38: Rule checking (all later)
Validation IFC file against XML definition
  Are only allowed entities delivered
  Have all required properties a (valid) value
This includes uniform enumeration values
Check if properties are reasonable (diameter between min/max)
  Diameter pipe for transporting water inside building <= 100 mm
Check if corresponding properies of elem and etyp match
  Is HeatEmission of etyp >= RequiredOutput of elem?
  Extra rule could be “within 20% margin”

## Slide 39: That’s all Folks