## Slide 1
CEN TC 442 WG2 | TG1
Building Information Modelling –
Level of Information Need

## Slide 3: Conceptual relationships 19650-1, 29481-1 and 17412-1

## Slide 4: The concept is defined in EN ISO 19650-1
level of information need – framework which defines the extent and granularity of information
Note 1 to entry: One purpose of defining the level of information need is to prevent delivery of too much information.
[SOURCE: EN ISO 19650-1:2018]
how much or how little information, and how detailed

## Slide 5: An overview EN 17412-1

## Slide 6
Define Requirements
Create information
Check

## Slide 7: Level of information need to be specified
Three types of information:
geometrical information – description of detail and extent of information that can be expressed using shape, size, dimension, and location
alphanumerical information – description of detail and extent of information that can be expressed using characters, digits and symbols or tokens such as mathematical symbols and punctuation marks
documentation – collection of documents related to a given subject

## Slide 8: Geometrical information
Detail
Dimensionality
Location
Appearance
Parametric behaviour

## Slide 9: Alphanumerical information
To specify the alphanumerical information for an object or a set of objects, the identification and information content should be specified.
Identification is used to position an object within a breakdown structure.
Information content is typically specified properties according to the defined purposes and the standards (EN ISO 23386 and EN ISO 23387).

## Slide 10: Documentation
The documentation for an object or set of objects to support processes, decisions, approvals and verification of information deliverables should be specified as a set of required documents.
Documentation is typically a collection of documents related to a given subject and/or to a purpose, e.g.
an application for building permit
a collection of models, drawings, specifications and tendering lists for tendering and bidding
The result of a phase or a process to be the basis for the next process

## Slide 11: Level of information need – 3 standards
Part 1 – Concepts and principles
Part 2 – Application
Part 3 – Data Schema